## Slide 1: RDCH 702 Lecture 8: Accelerators and Isotope Production
Particle generation
Accelerator
  Direct Voltage
  Linear
  Cyclotrons
  Synchrotrons
    Photons
      XAFS
      Photonuclear
  Heavy Ions
Neutrons sources
  Fission products and reactor
  Spallation

## Slide 2: Charged Particle Accelerators: Direct Voltage
Use of electric fields to accelerate particles
First used in 1932 for protons
Cascade Rectifiers and Transformers
  Direct application of voltage between terminals
    Maximum voltage defined energy limit
  Use multiple stages of voltage doubling circuits
Still used as injectors for high energy accelerator and neutron sources
Commercially produced

## Slide 3: Van de Graaff Generator
Electrostatic Generator
  All potential provide at one source
  Higher potential than direct voltage
First built in 1929,
  positive charges collected on a belt and used to charge a sphere
  equilibrium between build up and loss dictates charge on sphere
Ion source or electron gun produces ions or electrons which are focused into accelerating tube
Accelerating tube
  under vacuum
  sections of metal define path
  focused at ends of metal
Well focused beams can be produced
Magnetic analyzer may be needed to purify beam
  H+, H2+, H3+ all accelerated

## Slide 4: Tandem Van de Graaff Accelerator
Negative ions (H-) are accelerated towards positive terminal
Inside terminal ions are stripped of electrons
Positive ions further accelerated towards ground
Can couple more stages
Proton energies 25-45 MeV
Can also accelerate heavy ions

## Slide 5: Linear Accelerator
Repeated accelerations through small potentials
  Can use other accelerator output as source
Connection of coaxial sections
Alternating voltage
Ions accelerated at gap
First made in 1928
Range of cavities
  Constant or varied in size
    Traveling wave
    Standing wave
Electron accelerators on similar principle
  Pulsed machines
  Up to ­ 20 GeV
  Positron acceleration possible (at lower energies)
  Used for electron scattering, photonuclear reactions, radiation therapy, industrial processing
  SLAC around 2 miles

## Slide 6: Proton Linacs
Protons and other positive ions have large velocity increase with energy
Standing wave acceleration
Drift tubes need to increase in length
Acceleration at gap between tubes
Large energies (up to 800 MeV at LANSCE)
Use protons as production tool
  Mesons
  Neutrons
  Spallation products

## Slide 7: HILACS
Heavy ion linear accelerator at LBL
Construction similar to tandem Van de Graaffs
Accelerate all types of heavy ions, up to U
  Energies in range of 10 MeV/amu
  Used in
    relativistic experiments
    nuclear structure
    high energy nuclear collisions
    injectors

## Slide 8: Cyclotrons
First built in 1930
Multiple acceleration by potential
Ions travel in spiral
Alternation of “dee” potential accelerates particles
Obeys equations of motion
  mass m
  charge q
  velocity V
  magnetic field B
  radius R
angular velocity
Can control energy by varying terms
  R often fixed, B can be varied

## Slide 9: Cyclotrons
Fixed Frequency
  accelerates chosen e/M ratio
  different energies since M dependent
Sector focused
  useful for heavier ions
  creates hill and valley in regions
Cyclotrons can be combined with Linacs for high energy
eV

## Slide 10: Photon Sources
Continuous spectra of EM radiation is emitted when relativistic electrons are in a curved path in a magnetic field
    Relativistic velocity changes observed frequency due to Doppler effect
      Lorentz factor (g)
        Time contraction also increase frequency by g
    Forward directed radiation
can choose wavelength of photons
useful for determining structure
  IP, PES, EXAFS, XANES
Solid state physics
Reaction mechanisms
Perform many experiments simultaneously

## Slide 11: XAS Setup

## Slide 12: XANES and EXAFS
X-Ray Absorption Near Edge Spectroscopy (XANES)
Region between absorption edge and start of EXAFS oscillations, up to 40 eV above edge
Absolute position of edge contains information on oxidation state
Also contains information on vacant orbitals, electronic configuration, and site symmetry
Extended X-ray Absorption Fine Structure (EXAFS)
Above absorption edge, photoelectrons created by absorption of x-ray
Backscattering photoelectrons effect x-ray absorption
  Oscillations in absorption above edge
  Oscillations used to determine atomic number, distance, and coordination number of nearest neighbors

## Slide 13: Bacteria EXAFS
EXAFS and Fourier transforms. Slight structural differences can be seen.

## Slide 14: EXAFS Analysis
Structure is consistent with uranyl phosphate
Monodentate and bidentate P at 3.61 and 3.04 Å

## Slide 15: EXAFS Analysis
22 mM Sample
  Mixture of phosphate and acetate structures
  Due to high U concentration, phosphate possibly saturated

## Slide 16: Neutron Sources
Radioactive sources (252Cf, reactions)
Accelerators
  2H(d,n)3H
  3H(d,n)4He
    Neutron energy fast
  also (g,n) with 2H or 9Be
Alpha-neutron sources
  Pu-Be sources
Reactors
  specific design
  high amount of 235U

## Slide 17: Fission Process
Usually asymmetric mass split
  MH/ML1.4 for uranium and plutonium
  due to shell effects, magic numbers
    Heavy fragment peak near A=132, Z=50, N=82
  Symmetric fission is suppressed by at least two orders of magnitude relative to asymmetric fission
Occurs in nuclear reactions
  Competes with evaporation of nucleons in region of high atomic numbers
Location of heavy peak in fission remains constant for 233,235U and 239Pu
  position of light peak increases
2 peak areas for U and Pu thermal neutron induced fission
Influence of neutron energy observed
235U fission yield

## Slide 18: Fission Process
Fission yield distribution varies with fissile isotope
Heavier isotopes begin to demonstrate symmetric fission
  Both fission products at Z=50 for Fm
As mass of fissioning system increases
  Location of heavy peak in fission remains constant
  position of light peak increases

## Slide 19: Fission products
Primary fission products always on neutron-excess side of  stability
  high-Z elements that undergo fission have much larger neutron-proton ratios than stable nuclides in fission product region
  primary product decays by series of successive - processes to its stable isobar
Yields can be determined
  Independent yield: specific for a nuclide
  Cumulative yield: yield of an isobar
    Beta decay to valley of stability
  Data for independent and cumulative yields can be found or calculated
Comparison of cumulative and independent yields for A=141
http://www-nds.iaea.org/sgnucdat/c2.htm

## Slide 20: Fission Process
Nucleus absorbs energy
  Excites and deforms
  Configuration “transition state” or “saddle point”
Nuclear Coulomb energy decreases during deformation
  Nuclear surface energy increases
Saddle point key condition
  rate of change of Coulomb energy is equal to rate of change of nuclear surface energy
  Induces instability that drives break up of nucleus
If nucleus deforms beyond this point it is committed to fission
  Neck between fragments disappears
  Nucleus divides into two fragments at “scission point.”
    two highly charged, deformed fragments in contact
Large Coulomb repulsion accelerates fragments to 90% final kinetic energy within 10-20 s

## Slide 21: Proton induced fission
Energetics impact fragment distribution
excitation energy of fissioning system increases
  Influence of ground state shell structure of fragments would decrease
  Fission mass distributions shows increase in symmetric fission

## Slide 22: Review Notes
Describe accelerators
  Linear
  Cyclotrons
  Synchrotrons
    XANES and EXAFS
Describe utilization of photons from synchrotrons
Provide example of neutron sources
Comment in blog
Respond to PDF quiz